Real-Time Adaptive Signal Conditioning System for Wide Dynamic Range Inputs

Plain explanation
The diagram represents a Real-Time Adaptive Signal Conditioning System for Wide Dynamic Range Inputs.
The system automatically regulates the amplitude of an input signal by applying level-dependent gain control.
It continuously monitors the input signal level, compares it to a predefined threshold, and dynamically adjusts the gain of a voltage-controlled amplification stage to maintain the output signal within a controlled range.
The system operates in real time using a feed-forward control architecture, enabling fast	response to changes in input amplitude without directly feeding back the output signal.
II. Detailed explanation of how the system works

1. Signal Input

The system receives an analog input signal whose amplitude may vary significantly over time.

2. Voltage-Control
The input signal is fed directly into a Voltage-Controlled Amplifier.
This block applies a gain to the signal, where the gain value is controlled by an external control voltage. The VC is responsible for increasing or decreasing the signal amplitude in real time.
At this stage:
The signal path remains continuous
No frequency modification is intended
Only amplitude scaling is applied
3. Envelope Detector
In parallel with the main signal path, the input signal is routed to an Envelope Detector.
The purpose of this block is to extract a representation of the signal’s amplitude (or level), independent of its frequency content. This is typically achieved through rectification followed by low-pass filtering, producing a slowly varying control signal.
This block provides the system with real-time information about how “strong” the input signal is.

### 4. Signal Comparator
The output of the Envelope Detector is fed into a Signal Comparator, where it is compared against a predefined reference threshold level.
If the detected signal level is below the threshold, no gain reduction is required.
If the detected signal level exceeds the threshold, the comparator generates a control signal indicating that gain reduction should be applied.
This block implements the decision logic of the system.
5. Control Signal Generation
The output of the Signal Comparator is converted into a control voltage that determines how much gain reduction is applied by the VC.
The magnitude and timing of this control signal govern:
How quickly the system responds to increases in input level
How smoothly the gain returns to normal when the input level decreases
This behavior defines the system’s dynamic response characteristics.
6. Signal Output
The processed signal exits the system through the output block.
As a result of the adaptive gain control, the output signal exhibits a reduced dynamic range compared to the input, remaining within a controlled amplitude range even when the input varies significantly.
7. System block illustration
Fig. 1. block diagram
III. Deployment

1. Voltage-Control
Available methods
-Multi Variable Resistors Low Pass filtering
-Diode ladder filtering
Chosen Method:
Diode ladder filtering this method consists combining a multi set 2N2222 diodes in series will act as a variable resistance in function of the control-voltage applied to the input of the CV (V).
this method will cause less distortion and more control of the CV and its generally more cost-effective and easy to assemble.

1.1) schematic and functioning